## Slide 1: Stepper Motor Basics

## Slide 2: Common Motor Types
DC Motors
AC Motors
Other Motors
  Brushless
  Stepper
Watch Video Here

## Slide 3: Stepper Motor Anatomy
Watch Video Here

## Slide 4: Stepper Motor Wiring
Unipolar (5, 6, 8-lead)
  2 windings per phase
  Simpler to drive/control
  Current does not need to be reverse
Bipolar (4-lead)
  1 winding per phase
  More complex to drive/control
  Current must be reverse

## Slide 5: NEMA Motor Dimensions
Source
Motor | DD (mm) | a (mm) | b (mm) | c* (mm) | d (mm) | e* (mm) | f (mm) | g (mm)
NEMA 8 | 20.3 | 16 | 4 |  | 15 | 1.5 | 22.6 | 3
NEMA 11 | 27.9 | 23 | 5 |  | 22 | 2 | 32.5 | 4
NEMA 14 | 35.6 | 26 | 5 |  | 22 | 2 | 36.8 | 4
NEMA 17 | 43.2 | 31 | 5 | 24 | 22 | 2 | 43.8 | 4-40 UNC
NEMA 23 | 58.4 | 47.1 | 6.35 | 20.6 | 38.1 | 1.6 | 66.7 | 5
NEMA 34 | 86.4 | 69.7 | 9.5 | 31.8 | 73 | 1.6 | 98.4 | 5.5
NEMA 42 | 106.7 | 88.9 | 16 | 35.1 | 55.5 | 1.6 | 125.7 | 7.1
*max length

## Slide 6: Your NEMA 17
Bipolar, 4-lead
1.8° Step Angle
1.7 A current max
0.59 Nm holding torque
Vender

## Slide 7: Stepper Motor Control
Common Controllers
  A4988
  DRV8825
  TB6560AHQ
  TMC2130
Microstepping
  A4988 – 16th stepping
  DRV8825 – 32nd stepping
  TB6560AHQ – 16th stepping
  TMC2130 – 256th stepping
Interesting article about microstepping accuracy

## Slide 8: Your Stepper Motor Driver (A4988)
Pin 1 – Enable pin, Low is enabled
Pin 2 – Microstep selection pin 1
Pin 3 – Microstep selection pin 2
Pin 4 – Microstep selection pin 3
Pin 5 – Reset pin, Low resets
Pin 6 – Sleep pin, Low puts to sleep
Pin 7 – Step control pin
Pin 8 – Direction control pin, Low is CCW
Source
MS1 | MS2 | MS3 | Microstep Resolution
Low | Low | Low | Full step
High | Low | Low | Half step
Low | High | Low | Quarter step
High | High | Low | Eighth step
High | High | High | Sixteenth step
Vender

## Slide 9: Your Stepper Motor Driver (A4988)
Pin 9 – Ground
Pin 10 – Logic voltage supply, 5V
Pin 11 – Bipolar motor pin, coil 1B
Pin 12 – Bipolar motor pin, coil 1A
Pin 13 – Bipolar motor pin, coil 2A
Pin 14 – Bipolar motor pin, coil 2B
Pin 15 – Ground
Pin 16 – Motor voltage supply, 12V
Source
Vender
35V and 2A maximum rating

## Slide 10: Arduino Code
Source

## Slide 11: Arduino Code using AccelStepper
To install AccelStepper, go to Sketch > Include Library > Manage Libraries … and search for AccelStepper then select Install.
Source